## Slide 1: RPL-Observations
- Rahul (IETF 107)

## Slide 2: Updates
Added clarification with respect to “Trickle timer reset”
Backward Compatibility issues with new RPL Control Options

## Slide 3: DAO-ACK handling
Briefly the problem
  DAO-ACK is local in case of storing MOP
  Target not aware of E2E path establishment
  If a intermediate-6LR returns -ve DAO-ACK status, target is not informed of it.

## Slide 4: Proposition (draft-jadhav-roll-storing-rootack)
TIO = Transit Information Option

## Slide 5: Proposition (draft-jadhav-roll-storing-rootack)
Root sends the DAO-ACK back “directly” to target
  Target sets a flag in TIO to indicate Root to do this.
Address of target in Target Option
Root sends TIO option in DAO-ACK
  TIO needed for PathSequence
  Overall, just 1-bit change in TIO
TIO = Transit Information Option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = 0x06 | Option Length |E|K| Flags | Path Control |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Path Sequence | Path Lifetime | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ +

## Slide 6: Following points are considered
Handling Target aggregation in DAO
Handling multiple DAOs in progress with different PathSequence
Handling prefixes in Target Option
  How would a root know the Target address when the Target Option contains prefix?
What happens if a intermediate-6LR sends a -ve status in DAO-ACK?
Handling multiple preferred parents
Runtime memory efficiency
Incremental update possible: Root and subset of nodes can be upgraded.

## Slide 7: Next Steps
What’s the plan?
  DAO-ACK ... New draft in progress
Not sure how to organize
  DTSN handling ... best practices draft?
  Path control bits, lollipop counters (seq-window size recommendations, restart handling, worst case scenarios)
  Should we extend the current observations draft itself?
  Or a new draft with all combined?